## Slide 1: Dynamics of microdroplets under oscillatory and quasi-static deformation
Sanket Biswas
Supervisors: Dr. John M. Frostad, Dr. Gwynn J. Elfring
Department of Chemical and Biological Engineering The University of British Columbia, Vancouver, Canada 12 November 2025
MASc Thesis Defense

## Slide 2: Why microdroplets matter: targeted drug delivery
35M+ new cancer cases globally in 2050 (≈60% ↑ vs 2025)
Standard treatments → severe side effects
Alternative: targeted therapy with microdroplet drug carriers
Need: material properties of single microdroplets
Challenge: measuring properties of tiny, highly deformable droplets is difficult
Liyanage et al., Biochimica et Biophysica Acta (2019)
Microdroplet-based drug delivery
Yuan et al., Advanced Functional Materials (2024)
Drug-loaded microdroplets

## Slide 3: Macroscopic vs microscopic squeezing: bulk vs interfacial stresses
Singh et al., Physics of Fluids (2025)
Bell et al., Rheologica Acta (2006)
Oscillatory squeeze flow rheometer (OSFR)
Newtonian fluids:
Viscoelastic fluids:
Stefan (1875)
Phan-Thien (1980), Wingstrand et al. (2016)
Capillary number:
Elasto-capillary number:
small size, interfacial stresses important
large size, bulk stresses dominate
Notes: So a natural question is: when these microdroplets are squeezed through narrow vessels, which material properties control their flow and deformation, and why can’t we just use standard macroscopic rheometers to measure them?
To see this, let’s understand what traditional rheometers such as the oscillatory squeeze flow rheometer does: a centimetre-scale sample is confined between two plates, the upper plate is oscillated, and we measure the thin-gap force on the stationary lower plate.
For a Newtonian fluid, the force is proportional to the shear viscosity and the imposed deformation rate, so the response is set purely by bulk viscous stresses.
For a viscoelastic fluid, the force depends on the storage modulus 𝐺"′", which measures elasticity, and the loss modulus 𝐺"″", which measures viscous dissipation—again, only the bulk rheology enters, and this trend holds for essentially any macroscopic fluid.
This is because, for these macroscopic samples, the capillary and elasto-capillary numbers are generally much larger than one, so bulk viscous and elastic stresses overwhelm any stresses due to interfacial tension.
In contrast, for 10–100 µm droplets, those dimensionless numbers are order one or smaller, so capillary stresses become comparable to, or larger than, bulk stresses. So we really need squeezing experiments in this interfacially dominated regime to accurately characterize microdroplets.

## Slide 4: Squeezing of low-viscosity Newtonian droplets
Barakat et al., Physics of Fluids (2021)
(Laplace pressure + line interfacial tension)
(curvature stresses)
(bulk viscous stresses)
(microdroplet regime)

## Slide 5: CCFA: squeezing single microdroplets to measure material properties
Cantilevered capillary force apparatus (CCFA)
Frostad et al., Langmuir (2013)
Fixes a single soft microparticle/droplet (≈10 μm–1 mm) between its capillaries
Imposes controlled deformations:
  Oscillatory
  Quasi-static
  Uniaxial extension
Measures the force from the cantilevered capillary deflection
Oscillatory squeezing of viscoelastic microdroplets: CCFA theory?
Notes: The need to probe single viscoelastic microdroplets brings us to the cantilevered capillary force apparatus, or CCFA.
The CCFA holds a single soft microparticle or droplet between a rigid capillary and a flexible, cantilevered capillary, either by pinning it at the tips or by using suction.
Once it’s held, the rigid capillary can impose controlled deformations:
oscillatory squeezing, basically a microscale analogue of the OSFR,
very slow quasi-static deformations, where the droplet is essentially in equilibrium at each displacement,
and uniaxial extension, which I won’t discuss today.
As we deform the droplet, the cantilevered capillary bends, and from its deflection we obtain the time-dependent force 𝐹(𝑡). So CCFA gives us exactly what we wanted: controlled squeezing of a single microdroplet and a direct measurement of the deforming force. For Newtonian microdroplets, Barakat’s analytical work tells us exactly how to go from this 𝐹(𝑡) signal to material properties.
For viscoelastic microdroplets, that theoretical link is still missing — we don’t yet know how to turn this force signal into its bulk rheology and interfacial tension.
And since the CCFA can also do quasi-static deformations, we can ask a second, related question: for a simple Newtonian droplet, can we use its equilibrium force–displacement relation to extract its interfacial tension accurately?

## Slide 6: Quasi-static deformation: measuring interfacial tension
Linear model:
Quadratic model:
?
Kusumaatmaja and Lipowsky (2010)
Sariola (2019)
Notes: The need to probe single viscoelastic microdroplets brings us to the cantilevered capillary force apparatus, or CCFA.
The CCFA holds a single soft microparticle or droplet between a rigid capillary and a flexible, cantilevered capillary, either by pinning it at the tips or by using suction.
Once it’s held, the rigid capillary can impose controlled deformations:
oscillatory squeezing, basically a microscale analogue of the OSFR,
very slow quasi-static deformations, where the droplet is essentially in equilibrium at each displacement,
and uniaxial extension, which I won’t discuss today.
As we deform the droplet, the cantilevered capillary bends, and from its deflection we obtain the time-dependent force 𝐹(𝑡). So CCFA gives us exactly what we wanted: controlled squeezing of a single microdroplet and a direct measurement of the deforming force. For Newtonian microdroplets, Barakat’s analytical work tells us exactly how to go from this 𝐹(𝑡) signal to material properties.
For viscoelastic microdroplets, that theoretical link is still missing — we don’t yet know how to turn this force signal into its bulk rheology and interfacial tension.
And since the CCFA can also do quasi-static deformations, we can ask a second, related question: for a simple Newtonian droplet, can we use its equilibrium force–displacement relation to extract its interfacial tension accurately?

## Slide 7: Objectives: develop analytical frameworks to link microdroplet force response to material properties
Quasi-static deformation (Newtonian)
Nonlinear force and shape of a Newtonian microdroplet, enabling extraction of
Validate against numerical solutions
Oscillatory deformation (viscoelastic)
Small-strain, thin-gap force response of a viscoelastic microdroplet
Procedure to extract from the measured force

## Slide 8: Quasi-static deformation: governing equations
Force response:
Capillary separation:
Bridge volume conservation:
Notes: Let me now show how we model the quasi-static deformation problem. We start with an undeformed axisymmetric Newtonian microdroplet of radius 𝑅_𝑑 pinned between two capillaries of radius 𝑅. In the undeformed state the force is zero. When we slowly compress or dilate the droplet, always in equilibrium, viscous stresses die out and the force comes purely from line tension and Laplace pressure.
In dimensionless form, the normal force balance gives this relation between the force 𝐹 ̂, the mean curvature ℋ ̂, and the pinning angle 𝜃. So our unknowns are 𝐹 ̂, ℋ ̂, and 𝜃, and we need two more equations to close the problem.
The second equation is given by the Young–Laplace equation which connects the droplet shape to the capillary spacing 𝐿 ̂.
Finally, droplet volume is fixed due to mass conservation. For sufficiently small capillary radii, the relative change in the droplet bridge volume is very small, and, hence we impose this bridge volume conservation constraint.
Together these give a closed system, but the last two relations involve elliptic integrals, so they can’t be inverted in closed form.

## Slide 9: Regular perturbation in small displacement to avoid elliptic integrals
Force:
Mean curvature:
Pinning angle:
Small dimensionless displacement:
Notes: To deal with those elliptic integrals, as is standard, we focus on small deformations from the undeformed shape.
We introduce a small, dimensionless displacement 𝜀=Δ𝐿/𝑅_𝑑.
We then assume that the force response, mean curvature, and the pinning angle can all be written as regular perturbation expansion in 𝜀 about the undeformed spherical state.
Substituting these expansions into the three governing equations and collecting terms order by order in 𝜀 lets us solve algebraic equations, and gives us explicit first- and second-order corrections to the force and shape.

## Slide 10: Present quadratic model captures nonlinear force for all radii

## Slide 11: Analytical shapes match numerical profiles
Notes: So far I’ve shown that our quadratic model matches the force–displacement curves. But one of our objectives was also to capture the droplet shape. So, here I compare the analytical bridge profile to full numerical Young–Laplace solutions at a representative radius 𝑅 ̂=0.45, for three deformations: - strong compression, - moderate compression, and - dilation In each panel, the red curve is the numerical profile and the orange curve is the analytical prediction from our quadratic expansion. The two are essentially on top of each other in all three cases, so without solving the full Young-Laplace equation numerically, at moderate displacements we can recover the droplet shape just by knowing the initial pinning angle.

## Slide 12: Cubic error scaling ()
Notes: Having validated the force and shape, let’s examine how the error of our model scales—and how it stacks up against prior models.
In this absolute error versus displacement on log–log axes, the linear model admits a slope of about two, i.e., the error scales as 𝜀^2, which is expected. Sariola’s quadratic model shows the same slope because it proposed a weak quadratic correction by not including necessary shape corrections. Our model, once you’re past the tiny-displacement noise floor, admits a slope of about three, i.e., 𝜀^3 scaling—one order more accurate, as expected.
To further validate this scaling, we divide the error by displacement cubed and plot it against the normalized capillary radius. Curves taken at different displacements collapse onto a single smooth curve (black fit), which confirms the residual is cubic and primarily set by geometry.

## Slide 13: Oscillatory deformation: governing equations
Lubrication (droplet):
Maxwell (droplet):
Stokes (ambient):
Thin gap:
Small-strain:
Initial pinning angle:
Notes: Now we switch to describing the model for the oscillatory deformation of a viscoelastic microdroplet in a thin gap and small-strain regime.
First, to model the droplet’s shear stress distribution 𝜏 ̂, we use the most simple viscoelastic model, the Maxwell model—a spring and a dashpot in series—so the stress reflects both elastic storage and viscous relaxation. The relaxation modulus 𝐺 ̂ captures this dual solid–fluid behavior.
Next, because the droplet is oscillated in a thin gap, its motion is governed by the lubrication equations. In this setting the relaxation modulus plays the role that shear viscosity plays for a Newtonian thin film.
Finally, the ambient Newtonian fluid’s motion is modeled as Stokes flow at low Reynolds number.

## Slide 14: Oscillatory deformation: boundary conditions
Kinematic condition at interface:
No-slip on substrates
Interfacial stress balance:
Axisymmetric (regular at )
Quiescent far field
Thin gap:
Small-strain:
Initial pinning angle:
Notes: Now the boundary conditions.
First, as usual, no-slip on the substrates.
Second, axisymmetry with a regular centerline at 𝑟=0.
Third, a quiescent far field so the ambient fluid is undisturbed away from the gap—these three are the standard OSFR conditions. What’s special at the microscale is the interface.
The kinematic condition states the interface is material—there is no phase change—so, to leading order, the droplet shape is dictated by the radial lubrication velocity; any feedback of shape on the velocity appears only at higher order.
The interfacial stress balance states the jump in stress equals the capillary curvature stress: in the static limit this is Young–Laplace; at leading dynamic order, the droplet’s lubrication pressure balances the meridional curvature term—this is how interfacial tension enters. Bulk viscous stresses are subdominant in the thin-gap limit, so the ambient fluid plays essentially no role here. At high capillary numbers (macroscale OSFR), viscous stresses dominate and the condition reduces to an effective zero-pressure boundary.

## Slide 15: Force decomposition and limiting-case validation
(Laplace pressure + line interfacial tension)
(curvature stresses)
(bulk viscous stresses)
(bulk elastic stresses)
Phan-Thien (1980), Wingstrand et al. (2016)
Barakat et al. (2021)

## Slide 16: Material properties from force response
Static offset:
Amplitude:
Phase lag:
Notes: Let me now show how we model the quasi-static deformation problem. We start with an undeformed Newtonian microdroplet of radius 𝑅_𝑑 pinned between two capillaries of radius 𝑅. In the undeformed state the force is zero. When we slowly compress or dilate the droplet, always in equilibrium, viscous stresses die out and the force comes purely from line tension and Laplace pressure.
In dimensionless form, the normal force balance gives this relation between the force 𝐹 ̂, the mean curvature ℋ ̂, and the pinning angle 𝜃. So our unknowns are 𝐹 ̂, ℋ ̂, and 𝜃, and we need two more equations to close the problem.
The second equation is given by the Young–Laplace equation which connects the droplet shape to the capillary spacing 𝐿 ̂.
Finally, droplet volume is fixed due to mass conservation. For sufficiently small capillary radii, the relative change in the droplet bridge volume is very small, and, hence we impose this bridge volume conservation constraint.
Together these give a closed system, but the last two relations involve elliptic integrals, so they can’t be inverted in closed form.

## Slide 17: Key takeaways
Theory for nonlinear quasi-static force-shape of Newtonian microdroplets; infer interfacial tension
Theory for thin-gap, small-strain oscillatory force of viscoelastic microdroplets
Method to decouple interfacial tension and bulk rheology from measured force

## Slide 18: Acknowledgements

## Slide 19: Young-Laplace equation and parameterized bridge profile
Axisymmetric Young-Laplace equation:
First integral:
In terms of tilt angle :
Radial profile:
Axial profile:

## Slide 20: First-order coefficients

## Slide 21: Second-order coefficients

## Slide 22: Coefficient comparison

## Slide 23: Validity of the bridge volume conservation constraint

## Slide 24: Numerical scheme to solve the Young-Laplace equation
Parameterized bridge profile in terms of can be further parameterized in terms of the curvilinear arc length , leading to the ODE system:
Finn (1986), Moran et al. (1999)
Origin placed at the left capillary rim plane.
ODE system solved for a given force using the RK45 scheme, subject to the initial conditions:
unknown, a constraint is needed to fix it (shooting method)

## Slide 25: Numerical scheme to solve the Young-Laplace equation contd..
is iteratively adjusted in , and the ODE system is solved repeatedly while calculating the bridge volume via the trapezoidal rule, until it matches the zero-force volume:
Solver proceeds until the profile intersects the right capillary rim, defined by the boundary condition:
The stopping point gives us the capillary separation . The deviation of this value from the undeformed separation provides the dimensionless displacement .

## Slide 26: Present quadratic model significantly outperforms previous models

## Slide 27: Numerical & analytical mean curvature and agrees at different radii

## Slide 28: Validation: error for mean curvature and scales as

## Slide 29: Validation: numerical vs analytical profile for

## Slide 30: Validation: numerical vs analytical profile for

## Slide 31: Validation: numerical vs analytical profile for

## Slide 32: Validation: numerical vs analytical profile for

## Slide 33: Validation: numerical vs analytical profile for

## Slide 34: Maxwell linear viscoelastic model
Purely elastic spring
Hooke’s law of elasticity
Purely viscous damper
Newton’s law of viscosity
Shear modulus
Viscosity
Maxwell model
Relaxation time
Relaxation modulus:

## Slide 35: Intrinsic material properties of the viscoelastic microdroplet
Relaxation time:
Zero-shear viscosity:
Infinite-frequency modulus:
Deborah number:

## Slide 36: Non-dimensionalization scheme

## Slide 37: Relevant perturbation expansions
where
Cauchy stress tensor expansions:
Velocity field and dynamic pressure field expansions:

## Slide 38: Governing equations in complex space and dimensionless velocity and dynamic pressure fields
Lubrication equations in the complex space:
where the complex viscosity:
Dimensionless velocity field:
Dimensionless dynamic pressure field:

## Slide 39: Dimensionless force response
Dimensionless force response:
where the dimensionless numbers
Perturbation expansion of the force response:
where the static response:

## Slide 40: Interfacial stress balance

## Slide 41: Interfacial stress balance continued…

## Slide 42: Kinematic boundary condition and interface shape
Kinematic boundary condition for an interface:
Interface unit normal:
Outer unit normal:
Kinematic condition can be rewritten as: